## Slide 1
UNITED NATIONS GLOBAL GEODETIC
CENTRE OF EXCELLENCE
MODERNISING GEOSPATIAL REFERENCE SYSTEM
CAPACITY DEVELOPMENT WORKSHOP
Data registers and data sharing policies
Day 2, Session 3 [2_3_3]
HOW
Nicholas Brown
Head of Office, UN-GGCE
Acknowledgements: Michael Craymer (CAN); Roger Lott (IOGP); Liubov Poshyvailo-Strube (UN-GGCE); Scott Simmons (OGC).

## Slide 2
Introduction
ISO geodetic registry
EPSG geodetic parameter dataset
OGC registry
Summary and conclusions
Overview
The image is created by Liubov Poshyvailo-Strube with Microsoft Designer, https://designer.microsoft.com/

## Slide 3
Register – A structured database of information with unique identifiers
Registry – A registry is an office (or perhaps a web site)
The need for geodetic registers and registries:
To unambiguously identify the different coordinate reference systems and transformations used to manage geospatial data – primarily in GIS software
To foster interoperability of geodetic data and products
To support the implementation of the UN-GGIM Global Geodetic Reference Frame (GGRF)
GGRF Implementation Plan recommends Member States to publish their reference system definitions and transformations in the “ISO Geodetic Registry and other such registries as required to facilitate sharing of data and the interoperability of data and products with the GGRF”1
United Nations Committee of Experts on Global Geospatial Information Management: Road Map Implementation Plan, https://ggim.un.org/meetings/GGIM-committee/8th-Session/documents/Road-Map-Implementation-Plan.pdf. Accessed 28 January 2025.
Register and Registry

## Slide 4: OUTLINE
Introduction
ISO geodetic registry
EPSG geodetic parameter dataset
OGC registry
Summary and conclusions

## Slide 5: https://geodetic.isotc211.org
Maintained by the ISO Technical Committee on geographic information/ geomatics (ISO/TC 211)
Main purpose is to serve as the authoritative source for reference frames and transformation parameters
  Information in the ISOGR has been either directly entered or approved by the agencies responsible for defining and maintaining the reference systems and transformations
  Serves as an authoritative source for other registers (e.g., EPSG)
  Not meant to compete with other registries but complement them
ISO Geodetic Registry (ISOGR)

## Slide 6
ISOGR Control Body
Control Body of geodetic experts reviews and approves information to be published on the ISOGR
ISOGR Control Body is chaired by IAG representatives
  Chair: Michael Craymer
  Vice-chair: Larry Hothem
ISOGR Control Body is composed of geodetic experts appointed by TC 211 members
  28 members
  13 countries
  5 liaison organizations (IAG, FIG, PAIGH, OGC, CalConnect)
The Control Body meets monthly to review and approve the content for the ISOGR

## Slide 7
Built on ISO standards
Main standards include
  ISO 19111 “Referencing by coordinates”,
  ISO 19127 “Geodetic register”
  ISO 19135-1 “Procedures for item registration”
Other standards used for
  Date, time and coordinate formats
  Geography Markup Language (GML) output
  Text representation output
  . . .
ISOGR

## Slide 8
Submitting organization prepares proposal in collaboration with Control Body
Submit proposal
Register Manager reviews proposal for completeness
Control Body reviews proposal for correctness
Add to Register
Reject
Reject
Proposal approval process
Accept proposal
Approve proposal
ISO 19127 and ISO 19135 define procedures for preparing, managing, and maintaining the ISOGR
Types of submissions (proposals)
  Addition of new data
  Clarification or correction of existing data
  Supersession (i.e., updating) of existing data
  Retirement of existing data (i.e., no longer used but retained for historical purposes)
  Invalidation of existing erroneous data
For any questions: isogr@geodetic.org
Geodetic data registration

## Slide 9
Developed by
With support from
Current Content
977 register items
98 reference frames
32 vertical datums
275 geodetic CRSs
32 vertical CRSs
122 conversions
395 transformations
https://geodetic.isotc211.org

## Slide 10
 | Users | Returning | Pageviews
Jun-Nov 2019 | 681 | 14% | 441
Dec-Jun 2020 | 890 | 13% | 6507
Jun-Nov 2020 | 964 | 15% | 11826
Dec-Jun 2021 | 1158 | 24% | 6932
Jun-Nov 2021 | 1412 | 14% | 4960
Dec-May 2022 | 889 | -37% | 2980
Jun-Dec 2022 | 1,128 | 27% | 4755
Dec-May 2023 | 895 | -20% | 5010
Jun-Dec 2023 | 1,300 | 45% | 6691
Former ISOGR registry platform had
  Over 10 000 users since public release in 2019
  Over 10 000 page views per year
  Usage increased significantly in 2023
  Nearly half are now returning (regular) users
Registry migrated to a new platform in 2024
  More efficient for operation in the AWS cloud
  Will commence usage tracking again
ISOGR usage

## Slide 11
https://www.euref.eu/
Global ITRF geodetic datums (14) and CRSs (42)
Regional ETRF geodetic datums (11) & CRSs (33)
Regional EVRF vertical datums (4) & CRSs (4)
ITRF–ETRF transformations (33)
Examples for ETRF2020 on following slides
ETRF2020 datum
ETRF2020 LatLonEHt CRS
ITRF2020 to ETRF2020 transformation
EUREF content

## Slide 16
Over a thousand map projections for existing content
Reference frames used by GNSS systems
  WGS 84 – GPS (done)
  PZ-90 – GLONASS
  GTRF – Galileo
  CTRF 2000 – BeiDou
  JGS2010 – QZSS
National ETRS89 realizations
  Swedish SWEREF99 in progress – dynamic datum
  EUREF requesting members also add their national realizations
National SIRGAS realizations
  Colombia’s MAGNA-SIRGAS 2018 in progress
  SIRGAS-Chile realizations beginning
Planned new content

## Slide 17: OUTLINE
Introduction
ISO geodetic registry
EPSG geodetic parameter dataset
OGC registry
Summary and conclusions

## Slide 18: https://epsg.org/
European Petroleum Survey Group (EPSG)
  Online registry
  Holds data, has a graphic user interface (GUI) and an application programming interface (API)
  Data is stored in a data model which implements ISO 19111
EPSG Database
  EPSG Geodetic Parameter Dataset – the data in the EPSG registry
  The Dataset contains definitions of coordinate reference systems and coordinate transformations which may be global, regional, national or local
  One of the Dataset export options, MS Access used as carrier
  Dataset export also available as MySQL, Oracle or PostgreSQL scripts
  The Dataset is maintained by the Geodesy Subcommittee of the IOGP Geomatics Committee
EPSG registry

## Slide 19
EPSG content growth

## Slide 20
Each data record has a permanent code, i.e., an integer identifier
  EPSG code ranges from 1024 to 32766
  Data is never deleted from the EPSG Dataset, although minor corrections may be made (no code change)
  Anything with significant error will be deprecated and replaced with a new record with a new code. The deprecated record remains in the Dataset
EPSG codes are unique within each table (record type) of the data model
  But the same code value may be used in different tables
  Exception: codes are unique across union of CRS and coordinate operation tables **
To be unique, EPSG code and table (or entity type) should be cited as
  For example, “EPSG extent 1234” (= ‘Tonga – onshore and offshore’).
    “EPSG transformation 1234” (= a transformation applying to Uruguay).
  Code 1234 is also used in two other tables, datum and scope.
  No CRS has EPSG code1234, because it is used as a transformation (see ** above)
What are the EPSG codes?

## Slide 21
  Within the relational data model, they are used as a link to ‘component’ records in other tables
  For example, the GRS 1980 ellipsoid has a code: 7019, which is used to associate this ellipsoid with many reference frames
  Codes for these ‘component’ entities are primarily of use within the EPSG Dataset – they are not usually required by users
  Citation of identifier for ‘top level’ entities [CRSs and coordinate operations]
  Datasets associated with the same EPSG code can be merged without coordinate conversion or coordinate transformation.
  Using EPSG codes in this way is of special interest to data users
    to merge their datasets, they do not need the geodetic detail
    nor do they need the codes of the component entities (unit, ellipsoid, coordinate system, datum/reference frame, etc).
  To merge spatial datasets associated with different CRS codes requires conversion or transformation.
  In this context, the code can be used to obtain from the EPSG Dataset the information necessary for the conversion or transformation.
Purpose of the EPSG codes

## Slide 22
IOGP do not actively look for data – they react to requests
Requests can be made by anyone – see https://epsg.org/dataset-change-requests.html and https://epsg.org/guidance-notes.html
Population of the EPSG Dataset – submitting requests

## Slide 23
Procedure for accepting requests described in https://drive.tiny.cloud/1/4m326iu12oa8re9cjiadxonharclteqb4mumfxj71zsttwkx/736fcb2b-4b6e-4da7-b3ec-a00bc482d190 (EPSG Guidance Note 7-6)
  Data must be in public use.
  Information about the data must be in the public domain.
  Parameters are included in the EPSG Dataset
  Grid data files are cited by name, but the grid file itself is not in the EPSG Dataset (or held by IOGP)
  Data embedded in applications but not otherwise available is not included
So, if you feel that some data is missing, submit a request ! https://epsg.org/dataset-change-requests.html
Population of the EPSG Dataset – submitting requests

## Slide 24
‘non-ETRS’ national geodetic CRSs, projected CRSs and vertical CRSs [ → 100%]
  National geoid models [~40% populated, so ~60% missing  ]
Includes EVRF 2000, 2007 and 2019
  Transformations from national vertical CRS to EVRF2019 populated for ~55% of national vertical CRSs [~45% missing  ]
Includes ETRF89 … 2020
  Geodetic CRSs XYZ, φλh, and φλ – no projected CRSs
  Time-dependent transformations from ITRS taken from Memo and EUREF TN1
European data in the EPSG Dataset
(as of October 2024)

## Slide 25
National realizations of ETRS89 (densifications of ETRF)
  Included when given local name (green on map) [~50% of national realizations]
  Projected CRSs (UTM and national) based on these national realizations
  Missing when national documentation uses ‘EUREF’ or INSPIRE name ‘ETRS89’  e.g., Norway, Netherlands, Spain, etc. (unshaded on map)
Includes ETRS89 CRSs – based on datum ensemble
  UTM – E,N and N,E
  National projections for countries with missing national realization, e.g. Norway NTM zones
  LCC and LAEA (extent extended to include Azores, Madeira, Canaries, Iceland, Cypress, Turkey)
European data in the EPSG Dataset
(as of October 2024)
EUREF members can help with missing data ! 

## Slide 26
Geomatics Committee
  Technical reports and operational guidelines
  Data models
  Data exchange formats
  More information at https://www.iogp.org/workstreams/engineering/geomatics/
Geodesy Subcommittee
  Geodesy Guidance Notes
  More information at https://www.iogp.org/workstreams/engineering/geomatics/geodesy/
  Dynamic coordinate reference system video https://youtu.be/IKM-bR6SwVs
  GIGS open-source data driven testing framework https://gigs.iogp.org/
    Evaluate software application capability
    The objective of GIGS testing is to identify elements of software functionality that could result in failures of geospatial integrity.
Other IOGP resources supporting geodesy

## Slide 27: OUTLINE
Introduction
ISO geodetic registry
EPSG geodetic parameter dataset
OGC registry
Summary and conclusions

## Slide 28: https://www.ogc.org/
  The OGC standards help to ensure interoperability and seamless exchange of geospatial information across different systems and platforms
  OGC registry provides a machine-readable interface and serves as a Uniform Resource Identifier (URI) resolver for entries in the European Petroleum Survey Group (EPSG) registry
  It is overseen by the OGC Naming Authority
  Specific Earth Coordinate Reference System (CRS) content is managed by the CRS Domain Working Group (CRS DWG
  Planetary/astronomical CRSs content managed by the Planetary DWG
The displayed material if from the following publication:
Joint ISO/TC 211, OGC, IOGP. (2022). Guide to Coordinate Reference System (CRS) Resources, https://committee.iso.org/files/live/sites/tc211/files/Resources/GuideToCRSRegistries3.pdf. Accessed 3 February 2025.
OGC registry

## Slide 29
Also published as ISO 19111:2019
The foundation upon which all coordinate reference information is built in OGC and ISO / TC 211

## Slide 30
The CRS representation model for all OGC Standards

## Slide 31: OGC Registry for Accessible Identifiers of Names and Basic Ontologies for the Web (RAINBOW), https://defs.opengis.net/vocprez/
    OCS RAINBOW is
      An initiative by the OGC
      “Knowledge Graph”
      Concepts and Specifications
    OGC schema repository specifies the order, types and labels of information that describe geospatial datasets, https://schemas.opengis.net/
    Glossary of terms promote the use of common terminology, https://defs.opengis.net/vocprez/object?uri=http%3A//www.opengis.net/def/glossary
Notes: Imagine a scenario where multiple organizations are working together on a disaster response effort, such as coordinating relief efforts after a major earthquake. These organizations might include government agencies, non-profits, and international aid groups, each using different geospatial data systems and formats.
Without a tool like the OGC Rainbow, integrating and sharing this data could be challenging due to differences in terminology, data structures, and formats. This could lead to delays and inefficiencies in the response effort.
However, with the OGC Rainbow, these organizations can easily access a centralized platform that standardizes geospatial data concepts and vocabularies. This ensures that all parties are using consistent and interoperable data, facilitating seamless communication and coordination. As a result, relief efforts can be more efficient and effective, ultimately saving lives and resources.
In summary, the OGC Rainbow enhances interoperability, making it easier for diverse organizations to collaborate and respond to global challenges more effectively.

## Slide 32: OGC RAINBOW
Serves
      As a web-accessible source of information about concepts and vocabularies defined either by OGC or hosted on behalf of other communities
Applies
      FAIR (Findability, Accessibility, Interoperability, and Reusability) principles through a structured way of accessing and using geospatial data effectively
Provides
      Links between OGC and related domains
      Hosting for key resources from liaisons

## Slide 33: Why OGC RAINBOW?
“Normalizes” access to many types of resources
      As a web-accessible source of information about concepts
Supports better design
      Convergence
      Transparency of dependencies
      Consistency
The alternative is
      Chaotic
      Hard to navigate
      Non-machine-readable
      Unsustainable
Copy. Paste. Modify.
Invent your own.
Link. Profile. Reuse.

## Slide 34
GitHub repositories
      Local autonomy over content and process
Knowledge Graph(s)
      Online registries of content using common format
      Linking back to authoritative content
Web UI
      Navigation (Linked Data)
      Search, integration into other Web Resources
BuildingBlock Registries
      Richer UI bundling different types of resources in context of testing, playground and other development resources.
Where?

## Slide 35
The displayed material if from the following publication:
Joint ISO/TC 211, OGC, IOGP. (2022). Guide to Coordinate Reference System (CRS) Resources, https://committee.iso.org/files/live/sites/tc211/files/Resources/GuideToCRSRegistries3.pdf. Accessed 3 February 2025.
The geodetic registries do not compete, they complement each other
Geodetic data developers must adhere to generally accepted standards and practices to be able to add datasets to registries
The geodetic registry organizations welcome your contributions
Summary

## Slide 36: Q & A